## Slide 1: Software Implementation of LTE PHY.Layer.4G B.Sc. Graduation Project Supervisor Dr\Ahmed ABDULRAHMAN EMRAN
Al-Azhar University
Communication and Electronics Engineering

## Slide 2: Scanning of LTE.
LTE is the next generation of Mobile broadband technology.
Data rates of 100 Mbps.
It is the next level after UMTS 3G technology.
Works with IP (VOIP).
Provides low latency.
Focus on packet switched domain.

## Slide 3: LTE. Requirements
Peak bit (not data) rate – 100 Mbps DL/ 50 Mbps UL within 20 MHz bandwidth (i.e., SISO).
Up to 200 active users in a cell (5 MHz).
Less than 5ms user-plane latency condition (i.e., single user with single data stream).
Mobility – Optimized for 0 ~ 15 km/h. – 15 ~ 120 km/h supported with high performance. – Supported up to 350 km/h or even up to 500 km/h.
Spectrum flexibility: 1.5 ~ 20 MHz.
3GPP. Release 16

## Slide 4: LTE. Enabling Technologies
OFDM (Orthogonal Frequency Division Multiplexing) for Down Link.
Frequency domain equalization.
SC-FDMA (Single Carrier FDMA) for Up Link.
-Utilizes single carrier modulation and orthogonal frequency. -Multiplexing using DFT-spreading in the transmitter and frequency. domain equalization in the receiver. -A salient advantage of SC-FDMA over OFDM/OFDMA is low PAPR.
Efficient transmitter and improved cell-edge performance.
MIMO (Multi-Input Multi-Output).
-e.g., Open loop, Close loop, Diversity, Spatial multiplexing.
Multicarrier channel-dependent resource scheduling.
Fractional frequency reuse - Active interference avoidance and coordination
OFDM- SC.FDMA

## Slide 5: LTE. Radio protocol stack

## Slide 6: LTE. Downlink Physical channel

## Slide 7: Cyclic Redundancy Check
Error detection is the detection of errors caused by noise or other impairments during transmission from the transmitter to the receiver. Summer is another name for error detection. The receiver can detect a change in the original code word. • 1. The receiver has (or can find) a list of valid code words.
• 2. The original code word has changed to an invalid one.
• Cyclic codes are special linear block codes with one extra property. In a cyclic code, if a code word is cyclically shifted (rotated), the result is another code word. • A cyclic redundancy check (CRC) is an error-detecting code commonly used in digital networks and storage devices to detect accidental changes to raw data. • Blocks of data entering these systems get a short check value attached, based on the remainder of a polynomial division of their contents; on retrieval the calculation is repeated, and corrective action can be taken against presumed data corruption if the check values do not match.

## Slide 8: Cyclic Redundancy Check 24-a.of Noisy BPSK Data Frames in Simulink

## Slide 9
CYCLIC REDUNDANCY CHECK 24-A.OF NOISY BPSK DATA FRAMS IN SIMULINK – RESULT.

## Slide 10: Turbo Codes Channel coding

## Slide 11: What is turbo codes used for ?
It used for error detection and correction
Making higher Bit Error rate

## Slide 12: Overview
Turbo Encoder
Rate Matching

## Slide 13
Turbo encoder
structure
The scheme of turbo encoder is a Parallel Concatenated Convolutional Code (PCCC)
The turbo code rate is 1/3

## Slide 14
Interleaver

## Slide 15: What is the rate matching ?
The basic function of rate matching module is to match the number of bits in transport block(TB) to the number of bits that can be transmitted in the given allocation
It reduce the length of the code based on the channel behavior

## Slide 16: Rate Matching Structure
The rate matching consists of:
Sub-block interleaver
Circular Buffer
Bit Puncturing

## Slide 17: Sub-block interleaver
The sub-block interleaver randomize the data of the encoder output
For the systematic bits and the first parity bits we use a method of the interleaver
For the second parity bits we use another method of interleaver

## Slide 18: Circular Buffer
a single output buffer is formed by placing the rearranged systematic bits in the beginning followed by bit-by-bit interlacing of the two rearranged parity streams

## Slide 19: Puncturing
Puncturing is the process of removing certain symbols/positions from the codeword, thereby reducing the codeword length and increasing the overall code rate.
The puncturing is applied by a chosen P matrix
The overall code rate is R = ½
The commonly used P matrix is where the puncturing period is 2

## Slide 20
Turbo Decoder
RSC Encoder 1
RSC Encoder 2
MUX
π
Channel
DEMUX
Turbo
Decoding
u=[u1, …, uk, …,uN]
x
y
ys
y1p
y2p
u*
N-bit
Interleaver
xs
x1p
x2p
In the receiver, the turbo decoder inverts the operations performed by the turbo encoder
that turbo decoder depend on iterative operation

## Slide 21
Turbo Decoder
In the receiver, the turbo decoder inverts the operations performed by the turbo encoder
that turbo decoder depend on iterative operation
RSC Encoder 1
RSC Encoder 2
MUX
π
Channel
DEMUX
Turbo
Decoding
u=[u1, …, uk, …,uN]
x
y
ys
y1p
y2p
u*
N-bit
Interleaver
xs
x1p
x2p

## Slide 22
Turbo Engine

## Slide 23
Turbo Decoder
the idea of turbo decoding is using two soft input soft output (siso) decoders

## Slide 24
An Example of MAP Algorithm

## Slide 25
Turbo Code Error-Performance
Iterative decoding is a key feature of turbo codes. Each decoding iteration results in additional computations and decoding delay
number M is chosen, and each frame is decoded for M iterations
Usually, M is set with the worst corrupted frames in mind

## Slide 26: Orthogonal frequency-division multiplexing (OFDM)

## Slide 27
History Of Ofdm
OFDM is a frequency-division multiplexing (FDM) scheme that was introduced by Robert W. Chang of Bell Labs in 1966.
improved by Weinstein and Ebert in 1971 with the introduction of a guard interval.
802.11a was one of the first standards issued under the 802.11 umbrella in 1999.

## Slide 28
Evolution of Wireless Communication Standards
OFDM

## Slide 30: Ofdm Diagram

## Slide 31
Orthogonality of Sub-Carriers
The FFT is given by the equation
The IFFT is given by the equation

## Slide 33: Multipath Fading
Communications over wireless channels suffer from multi-path propagation
Multi-path channels are usually frequency selective
OFDM supports high data rate communications over frequency selective channels
From “Wireless Communications” Edfors, Molisch, Tufvesson

## Slide 34: Multipath Fading

## Slide 35: Inter Symbol Interference (ISI)
Inter symbol interference (ISI) occurs when a pulse spreads out in such a way that it interferes with adjacent at the sample instant.
we have two main problems from multipath .
  Interference between adjacent symbols (Inter symbol interference).
  Interference between different copies of the same data (Intra- symbol interference).

## Slide 36: Intersymbol Interference in OFDM

## Slide 37
Guard Time eliminates ISI between neighboring OFDM symbols
However each OFDM symbol suffers from inter-carrier interference (ICI)
Guard time corresponds to a reduction of bit rate
OFDM Symbol
Guard Time
Ts
Ts/4
Tx Signal
No ISI
Ts
Ts/8
Rx Signal
Suppose multi-path channel with delay Ts/8
h0
h1
Ts/8
Guard Time
Ts
Ts/4
Ts
Ts/8
Inserting Guard Time

## Slide 38
Cyclic Prefix (CP)
The basic concept behind the OFDM cyclic prefix is quite straight forward.
The cyclic prefix performs two main function.
The cyclic prefix provides a guard interval to eliminate inter symbol interference from the previous symbol.
It repeats the end of the symbol so the linear convolution of a frequency-selective multipath channel can be modelled as circular convolution.
The cyclic prefix is created so that each OFDM symbol is preceded by a copy of the end part of that same symbol.
Different OFDM cyclic prefix lengths are available in various systems. For example within LTE a normal length and an extended length are available and after Release 8 a third extended length is also included, although not normally used

## Slide 39: Cyclic Prefix
Ts
Ts/8
+
Tx Signal (Guard Time)
Tx Signal (Cyclix Prefix)
The cyclic prefix is used to eliminate Inter-carrier interference
Cyclic Prefix
Cyclic Prefix
Cyclic Prefix
OFDM Symbol
Guard Time
Ts
Ts/8
+
OFDM Symbol
Ts/8

## Slide 40
Consider the receiver for f1=1/Ts that correlates over Ts with
Ts
x
Orthogonal
No Inter-Carrier Interference
Rx Signal (Cyclix Prefix)
+
Cyclic Prefix
Correlation at Rx over Ts
Ts
Ts/8
Ts/8

## Slide 41
Team Names
Mohamed Ahmed Mahmoud Ahmed Khedawy
Mohamed Soliman Alsaid Soliman Hassab
Ahmed Hamdy Abdelfattah Saber Alesh
Ahmed Mohamed Abdulrahman Elwan
Mohamed Saied Mohamed Osman
Mohamed Magdi Soliman Hamda